## Slide 1: Forwarding Table
ADITHYA RAGHUNATHAN, GABE KROCH, CHIN JIE LIM, ERIC EWING

## Slide 2: Content Addressable Memory (CAM)
1 48-bit comparator for each entry – comparing input address with the CAM entries
  32 comparators in total
Valid/expired bit
Bit to indicate waiting-for-source address
Each entry will have concatenated source address + port
Clarifications:
  Is there a need to keep track of LRU entries?

## Slide 3
Forwarding Port
Forwarding Table
Look-Up Table
Comparator
LRU
Ageing

## Slide 4: Main Module (Look-Up System) In/Outputs
  Outputs
    isHit – address found in CAM
    Port
    Missed Port (for flooding)
    Missed Address (for flooding)
  Inputs
    Address (in first two cycle)
      Source & Destination
    Port (in subsequent cycle)
    “Look now” signal*
    Clock?*

## Slide 5: External Interface (Look-Up Table)
Submodules:
  Hash-Table
  Eviction
  Comparator
  Outputs
    n-bit Destination Port
    48-bit Destination Address
    isHit
    “Look-now” Signal
  Inputs
    48-bit Source Address
    n-bit Source Port
    48-bit Destination Address
    “Look-now” Signal
    Clock

## Slide 6: Internal Submodule: Hash-Table
Hash-table Implementation
2 Buckets per Hash-Key
2 Stage CRC: 3 Parallel CRCs, followed by a final CRC to obtain a 5-bit hash key
Contains a Valid Bit per Hash Entry
2-bit LRU per Hash Entry
  Outputs
    n-bit Destination Port
    48-bit Destination Address
    48-bit Address No.1 (to Comparator Subsystem)
    48-bit Address No.2 (to Comparator Subsystem)
    resetAgeing (to Eviction Subsystem)
    isHit
  Inputs
    48-bit Source Address
    n-bit Source Port
    48-bit Destination Address
    “Hash-now” Signal
    Clock
    ageOut (from Ageing)
    6-bit Non-Valid Signal
    2-bit Identifier (from Comparator)
    compareDone (from Comparator)

## Slide 7: Internal Submodule: Comparator
2 48-bit Comparators
MUX
  Outputs
    2-bit Identifier (to Hash-Table)
    compareDone (to Hash-Table)
  Inputs
    48-bit Address No.1
    48-bit Address No.2 (from the same Hash Bucket)
    5-bit Hash Entry

## Slide 8: Internal Submodule: Ageing
  64 9-bit Counters (300 seconds)
  Decoder for 6-bit Reset Signal
  Outputs
    6-bit Non-Valid Signal (Hash-Table)
    “Age-now” Signal (to Hash-Table)
  Inputs
    6-bit Reset Signal
    “Look-now” Signal

## Slide 9: Interfaces
Who is handling timing? E.g. when is the data going to be passed, are we running on the same clock?
How are we passing data?
Are we handling the read and write commands?
A signal to indicate “look-now” from the receiving port

## Slide 10: Questions
1) How fast does the table need to operate?
2) Does the table require buffering (for either side)?

## Slide 11: Roles & Timeline
Roles:
Ageing: Gabe
Comparator: Eric
External Interface & Hash-Table: Adi & CJ
Checkpoints:
Feb 21: Skeleton Code for each Submodule
March 7: Low-level Design Progress Report + Working Submodules
March 23: Integrated Submodules
April 6: Begin Integrating with Forwarding Subsystem