## Slide 1: Forwarding Table
ADITHYA RAGHUNATHAN, GABE KROCH, CHIN JIE LIM, ERIC EWING

## Slide 2: Content Addressable Memory (CAM) vs Hash Table
Hash Table – Trivial Eviction Policy
CAM – Requires LRU Implementation
1 48-bit comparator for each entry – comparing input address with the CAM entries
  32 comparators in total
Valid/expired bit
(CAM-Only) Bit to indicate waiting-for-source address
Each entry will have concatenated source address + port
Trade-Off:
  Design Simplicity vs LRU Accuracy/Temporal Locality/Hit Rate

## Slide 3: Main Module (Look-Up System) In/Outputs
  Outputs
    isHit – address found in CAM
    Port
    Missed Port (for flooding)
    Missed Address (for flooding)
  Inputs
    Address (in first two cycle)
      Source & Destination
    Port (in subsequent cycle)
    “Look now” signal*
    Clock?*

## Slide 4: Functional Subsystems (Aging System Design)
Scale down the clock, store as n-bit
Each entry will be associated with a timer
Timer will be reset everytime an external destination entry is detected
Output as 32-bit (set to reset the CAM entry, and directly associated to the CAM)
  Outputs
    32-bit
  Inputs
    Index [N – 1 : 0]
    WriteEnable (“LookNow”)

## Slide 5: Functional Subsystems (Possible Eviction System Design)
Keeps track of LRU (FIFO Queue/Buffer)
Offers up the LRU entry for eviction when entries exceed CAM entry size
Ports
  Input
    moveToBack
    addToQueue[4:0]
  Output
    isFull
    evictIndex[4:0]
IMPLEMENTATION? FIFO QUEUE NOT SUFFICIENT?

## Slide 6: Interfaces
Who is handling timing? E.g. when is the data going to be passed, are we running on the same clock?
How are we passing data?
Are we handling the read and write commands?
A signal to indicate “look-now” from the receiving port

## Slide 7: Roles & Timeline
To be determined after clarifications and subsystem functions are fully determined